## Slide 1
T-RECAP System Architecture
Team #2
DE1-SoC | FPGA signal processing with ARM control and telemetry
FPGA / STFT–WOLA CORE
INPUT
BRAM replay
or audio line-in
Window + FFT
Time to frequency
Threshold mask
Select retained bins
IFFT + WOLA
Reconstruct signal
Programmable spectral suppression with continuous reconstruction
Telemetry FIFO
Never stalls the core
DDR ring
Shared buffer
ARM HPS
Control + UDP
PC
Dashboard
BUFFERED OBSERVATION PATH
FPGA processes signals. ARM handles control and transport.
Notes: Team #2
60-second narration script
Hi, I'm presenting for Team Two. This slide shows the architecture of our T-RECAP project on the DE1-SoC.
Samples come from stored test data or an audio input. The FPGA applies a window and FFT, uses a programmable threshold to suppress selected frequency bins, then reconstructs the signal with an inverse FFT and weighted overlap-add.
A separate telemetry path sends data through DDR memory to the ARM processor without stalling the core. ARM forwards the data over Ethernet to our PC dashboard and configures the FPGA through control registers.
We compare numerical results against an independent reference model. Our next steps are completing system validation and measuring energy use.
Architecture notes
STFT = short-time Fourier transform. WOLA = weighted overlap-add. BRAM replay is the repeatable baseline source. Audio line-in is an alternate source. The compressed diagram omits source selection, canonicalization/spectrum construction, the DDR record writer, and the reverse configuration connection. ARM writes FPGA control registers at safe boundaries. Telemetry is best effort and may drop records under congestion rather than stall the processing core. The C++ model is a reference model, not a certified golden model. Spectral masking alone is not evidence of lower measured electrical energy. The FPGA core performs FFT, masking, IFFT, and WOLA. The ARM processor handles control and transport.
Sources
Project architecture and RTL: T_RECAP_Phase2_R1_delay_history_fix_v70, rtl/core/trecap_core_top.sv, processing-chain declarations and instantiations. See the project architecture document for the complete system and control paths.
ASU Brand Guide, Color: https://brandguide.asu.edu/brand-elements/design/color (maroon #8C1D40 and gold #FFC627).